## Slide 1: The ideal and reality of NVDIMM RAS
Yasunori Goto / QI Fuli
Linux Development Division
Fujitsu Limited
China Linux Kernel
Developer Conference
Oct 14, 2018

## Slide 2: Agenda
Introduction of NVDIMM
Issues of RAS which we found and solved
  Distinguish and replace broken NVDIMM (by Yasunori Goto)
  Monitoring feature of NVDIMM (by Qi Fuli)

## Slide 3: Introduction of NVDIMM

## Slide 4: NVDIMM is coming
Non Volatile DIMM (NVDIMM)
  Some vendor released / will release NVDIMM
    Intel Optane DC persistent memory
  CPU can read/write NVDIMM directly like RAM
  Data is not volatile even if system is powered down
  Though its access latency is a little slower than DRAM, it is expected to be very faster than NVMe
  May be huge amount (*)
Use case
  For example, On memory Database
  (*) It depends on type of NVDIMM

## Slide 5: Impact of NVDIMM
Traditional I/O layer is not suitable for NVDIMM
  Page cache is not necessary at least
    It was created for SLOW I/O storage
    But, it is just redundant for NVDIMM
  Even system call may be waste of time due to switch kernel mode and user mode
    Ideal is that application can access to NVDIMM directly without kernel
  If application calls cpu flush instruction, then data becomes persistent
    calling sync()/fsync()/msync() becomes redundant
To achieve the above feature, New access method is expected
  DAX (Direct Access Mode) is developed in Linux

## Slide 6: Filesystem is still useful for traditional software
On the other hand, Many software assumes that memory is VOLATILE
    They allocate memory areas on the RAM and make structures on them
    When allocate memory area on the NVDIMM like RAM, what will happen?
  For NVDIMM, many things are necessary. For example
    Need data structure compatibility on NVDIMM
      Should not change data structures in NVDIMM
      If the structures are changed, software update will be cause of disaster
    Need to detect / correct collapsing data
      CPU cache is still volatile. If system power down suddenly, then some data may not be stored
      If the data is broken, software need to detect it and correct it
Filesystem is still useful for traditional software
  Filesystem gives many solution for the above considerations
    Format compatibility of filesystem, data correction, region management, , authority check, etc...

## Slide 7: Interfaces of NVDIMM
Linux provides some interfaces for application
  Storage Access
    Application can access NVDIMM via traditional I/O
    This mode is for old application
  Filesystem DAX(*) and Device DAX
    Application can read / write NVDIMM area directly if it calls mmap()
    Need modification or making new software
  PMDK is provided
    libraries and tools for software which uses DAX
DAX enabled filesystem
NVDIMM
user layer
kernel layer
Pmem (or block window) driver
device dax driver
/dev/dax
New App with Device DAX
BTT driver
Traditional filesystem
Traditional App
New App with Filesystem DAX
PMDK
management command
sysfs
ACPI driver
ACPI
(*) DAX= Direct Access Mode

## Slide 8: Region and Namespace(1/2)
To manage huge amount of NVDIMM, “Region” and “namespace” is defined
  Region
    Region is created by hardware and firmware feature
    Each NVDIMM modules are placed on a System Board(Mother Board)
    You can create regions on NVDIMM modules
      Interleave is available
region 1
region 2
region 0
(This is
Interleaved region)
System Board
NVDIMM module1
NVDIMM module2
NVDIMM module 3

## Slide 9: Region and Namespace (2/2)
  Namespace
    You can create namespaces on each region by ndctl command
      Namespace concept is likely LUN of SCSI
      You can make plural namespaces on a region, if you wish
      You can specify storage, filesystem-dax, or device dax at this time
    NVDIMM driver names each NVDIMM module “nmemX”
    /dev/pmemX or /dev/daxY is named for each namespace
      If Storage mode or Filesystem DAX, you can make partition and filesystem on the /dev/pmemXXX
region 1
region 2
System Board
NVDIMM module1
(nmem1)
NVDIMM module2 (nmem2)
NVDIMM module 3 (nmem3)
namespace0.0
/dev/pmem0
namespace1.0
/dev/pmem1s
namespace1.1
/dev/pmem1.1
namespac2.0
/dev/dax2
(region 0)

## Slide 10: Management command
ndctl
  Many features
    Create / Manage namespaces
    Set access mode (storage / Filesystem DAX/ Device DAX)
    Show status of NVDIMM modules, regions, namespaces
      Support difference among NVDIMM vendors (NVDIMM-N or 3D-xpoint...)
    etc..
  It use ACPI via sysfs and acpi driver for NVDIMM (nfit.ko)
We add some feature in it for RAS
DAX enabled filesystem
NVDIMM
user layer
kernel layer
Pmem (or block window) driver
device dax driver
/dev/dax
New App with Device DAX
BTT driver
Traditional filesystem
Traditional App
New App with Filesystem DAX
PMDK
ndctl
sysfs
ACPI driver
ACPI
NVDIMM
ACPI

## Slide 11: ACPI spec for NVDIMM
ACPI v6.0 or later supports specification for NVDIMM
  NFIT table is defined for NVDIMM
    Many sub tables are specified for NVDIMM basic information
      (Very huge table)
  In DSDT
    Some specification of NVDIMM is defined
    “NVDIMM root device”
      defined for whole system
      Its _DSM method has some features like Address Range Scrubbing
      Notification is used for NFIT update or Memory error detection
    “NVDIMM device”
      defined for each NVDIMM modules
      Its _DSM method is used for manage namespace or Health (SMART) information, etc.
      If health status is changed, firmware notifies a event to the “NVDIMM device” in DSDT
      There is a little bit difference among vendors (Intel) http://pmem.io/documents/NVDIMM_DSM_Interface-V1.7.pdf (HPE) https://github.com/HewlettPackard/hpe-nvm

## Slide 12: Replacement of NVDIMM
Issues and what I solved

## Slide 13: NVDIMM may be broken
We need to consider when NVDIMM becomes broken
  The life of NVDIMM is limited
    Write endurance of NVDIMM is / will be not infinite
    NVDIMM module has / may have some feature
      wear leveling
      spare blocks instead of broken block
      If spare block is consumed completely, the NVDIMM modules can not recover
    NVDIMM-N has a battery in the module
      It will be also deteriorated
  Bit error may also occur on NVDIMM
    “Scrubbing” feature may rescue it from fatal error if possible
      If it can not rescue, the block becomes broken
We need to have a way to replace broken NVDIMM

## Slide 14: Question
Please imagine a difference between HDD/SSD and NVDIMM
  How to replace its device?

## Slide 15: Answer
There is a difference between SSD/HDD and NVDIMM replacement like the followings
HDD/SSD
A disk unit is removable without opening the cover of box
Hot-replace is enabled by hardware (hotplug slot, electric switch, etc)
Device Mirroring is helpful for replacing the device
NVDIMM
You need to open the cover of box to replace NVDIMM
Hardware does NOT support hot-replace for NVDIMM
No hardware mirroring for NVDIMM (at least, currently)
  In addition, you can not use Software RAID with Filesystem DAX or Device DAX
Replacing of NVDIMM is more difficult than SSD/HDD

## Slide 16: Replacing broken NVDIMM is complex (1/2)
In addition, the specification of NVDIMM (region and namespace) is cause of more difficulty of replacement
  In this figure, when a block on region 0 is broken eternally, and user need to replace it, what information is necessary?
Copyright 2018 FUJITSU LIMITED
region 1
region 2
System Board
NVDIMM module1
(nmem1)
NVDIMM module2 (nmem2)
NVDIMM module 3 (nmem3)
namespace0.0
/dev/pmem0
namespace1.0
/dev/pmem1s
namespace1.1
/dev/pmem1.1
namespac2.0
/dev/dax2
broken
(region 0)

## Slide 17: Replacing broken NVDIMM is complex(2/2)
  To replace broken NVDIMM, the following information is necessary, at least
region 1
region 2
System Board
NVDIMM module1
(nmem1)
NVDIMM module2 (nmem2)
NVDIMM module 3 (nmem3)
namespac0.0
/dev/pmem0
namespace1.0
/dev/pmem1s
namespace1.1
/dev/pmem1.1
namespac2.0
/dev/dax2
broken
Need a way to distinguish which NVDIMM module is broken (especially, if the region is interleaved, only firmware know it)
To replace NVDIMM, Need information of relationship between “Physical” location of NVDIMM module (Ex. Silk print on mother board), and Device name of namespace /dev/pmemX)
Need to know other namespace on same DIMM modules for backup before replace
(region 0)

## Slide 18: What I developed
I made 2 features of ndctl
  To show important information for replace
region 1
region 2
region 0
System Board
NVDIMM module1
(nmem1)
NVDIMM module2 (nmem2)
NVDIMM module 3 (nmem3)
namespac0.0
/dev/pmem0
namespace1.0
/dev/pmem1s
namespace1.1
/dev/pmem1.1
namespac2.0
/dev/dax2
broken
Show NVDIMM info which has broken block in the region
Show the id of NVDIMM module to find physical location
Fortunately, current ndctl can show
all namespaces on a NVDIMM already,
(I will mention how to do it later)

## Slide 19: To show broken NVDIMM
ndctl did not show broken NVDIMM module information
  It just showed broken “block number” in the region
  When the region is Interleaved, kernel/driver cannot distinguish NVDIMM
    Only firmware know the relationship between physical address and NVDIMM module
  Fortunately, “Translate SPA” is defined in _DSM method of “NVDIMM root Device” at ACPI ver.6.2
    Firmware translates from System Physical Address to “NFIT DIMM handle” and Physical address in the DIMM( DPA)
I made the following translation in the ndctl
block number of the region
Its System Physical address
Get NFIT DIMM handle
NVDIMM
device name
(nmemX)
ndctl
firmware
call _DSM Transrate SPA

## Slide 20: display bad block information (1/2)
# ndctl list -DRHMu
{
"regions":[
{
"dev":"region0",
"size":"250.00 GiB (268.44 GB)",
:
"mappings":[
{
"dimm":"nmem1",
:
},
{
"dimm":"nmem0",
:
}
],
:
(cont)
region 0 is
interleaved region
by nmem1 and nmem0
command to show
region info with
dimm, health and bad block info
(output is JSON format)

## Slide 21: display bad block information (2/2)
:
],
"badblock_count":1,
"badblocks":[
{
"offset":65536,
"length":1,
"dimms":[
"nmem0"
]
}
],
:
:
#
Current ndctl displays
which DIMM has badblock
in this region
In this example,
nmem0 has broken block
badblock info in the region
(the previous ndctl showed only this information)

## Slide 22: To show NVDIMM device location (1/2)
What can shows the physical location of NVDIMM modules?
  /dev/nmemX is named for NVDIMM module by NVDIMM driver
    It is also used by ndctl
    However, its id (X) is not related with device location
      The driver decided it by the order which it found
  I thought the handle of “NVDIMM Device” in ACPI DSDT may be good
    Handle is created with the followings
      node controller id, socket id, memory controller id, etc...
    However, these id may be dynamic due to hardware/firmware configuration
      Especially, our some servers can change # of nodes by dividing the box with system configuration
      So, this may not be good to find physical location too

## Slide 23: To show NVDIMM device location (2/2)
  The remaining option is SMBIOS handle
    You can confirm physical location of a device with “dmidecode” command
      In addition, each device has SMBIOS handle, and shown in the command
    SMBIOS handle is also “NVDIMM Region mapping structure” table in NFIT
    So, if ndctl command can show it, you can find the location with the handle
    I made a patch that ndctl show it as phys_id

## Slide 24: Example of SMBIOS Handle of ndctl
# ndctl list -Du
[
{
"dev":"nmem1",
"id":"XXXX-XX-XXXX-XXXXXXXX",
"handle":"0x120",
"phys_id":"0x1c"
},
{
"dev":"nmem0",
"id":"XXXX-XX-XXXX-XXXXXXXX",
"handle":"0x20",
"phys_id":"0x10",
"flag_failed_flush":true,
"flag_smart_event":true
}
]
display DIMM infomation
with human readable format
(phys_id becomes Hexadecimal)
phys_id is SMBIOS handle of these DIMM
0x10 is broken DIMM’s handle
in this example
(The nmem0 included broken block
in previous result)

## Slide 25: dmidecode can show the location of DIMM
# demidecode
:
Handle 0x0010, DMI type 17, 40 bytes
Memory Device
Array Handle: 0x0004
:
:
Locator: DIMM-Location-example-Slot-A
:
Type Detail: Non-Volatile Registered (Buffered)
SMBIOS handle of DIMM
Locator: shows the place of the DIMM

## Slide 26: How to distinguish all namespaces on the DIMM
ndctl list command has many filtering feature
  by region, namespace, bus, and dimm
  Then list namespace with filtering dimm by ndctl, you can find all the namespaces
# ndctl list -N -d 0
[
{
"dev":"namespace0.2",
"mode":"sector",
"size":67042312192,
:
},
{
"dev":"namespace0.0",
"mode":"sector",
"size":67042312192,
:
}
]
command to show
all namespaces on the nmem0
This dimm includes 2 namespaces
You need to back up them
before replacing nmem0

## Slide 27: NVDIMM Monitoring Daemon
ndctl monitor
Notes: OK, now it is my turn to talk about the nvdimm monitoring daemon.

## Slide 28: Who am I?
QI Fuli
  Software Engineer at Fujitsu Ltd.
  PhD Student at University of Tokyo
  Working on R&D of PM
  Email: qi.fuli@fujitsu.com
Notes: Before my speech, please allow me to introduce myself a bit.
My name is QI Fuli. I am a software engineer at Fujitsu, meanwhile a phd student at university of Tokyo. Currently I am working on the persistent memory Research and development.

## Slide 29: Why the status of NVDIMM must be monitored?
NVDIMM has a life span
  Blocks of NVDIMM will be broken due to endurance problem
  NVDIMM modules consume spare block
  When spare decreases to 0, it can not rescue broken block
  NVDIMM has no feature such as mirroring to save its data
Backup and replacement is needed before no spares
Users should know the best time to do the backup and replacement
Status of NVDIMM needs to be monitored and be notified before NVIMM becomes broken
Notes: First, I want to explain why the status of NVDIMM must be monitored.
Same as NAND Flash, NVDIMM has a life span, and blocks of NVDIMM will be broken due to endurance problem. The more I/O operations are performed, the more likely it is that NVDIMM’s blocks will break. NVDIMM modules consume spare block. In case of that a block breaks, its data will be swapped to spare block. With the increase of broken blocks, the amount of spare is decreasing. when the spare decrease to 0, it can not rescue the broken block. That is to say, the NVDIMM will be broken.
NVDIMM does not have a feature, such as memory-mirroring to save their data when it becomes broken. There is no HW mirroring at this phase. SW RAID only supports the usage of traditional OS storage stacks, rather than FS Dax or device DAX. Therefore the data will be lost when NVDIMM becomes physically damaged.
It is necessary to backup its data and do the replacement before there is no spare in NVDIMM. Therefore, the data can be prevented from NVDIMM physical damage.
Users need to know the best time to backup the data and replace the broken NVDIMM. In a word, Status of NVDIMM needs to be monitored and be notified before NVIMM becomes broken.

## Slide 30: Ndctl monitor
I created a daemon to monitor NVDIMM
  monitor health status
  notify critical status
  https://pmem.io/ndctl/ndctl-monitor.html
NVDIMM will be broken !!! Spare block ratio is low !!!
blocks
spares
5%
Notes: Users need to know the best time to backup the data and replace the broken NVDIMM. In a word, Status of NVDIMM needs to be monitored and be notified before NVIMM becomes broken.
Here I created a daemon to monitor NVDIMMs. We call it ndctl monitor and make it as a subcommand of ndctl command. Ndctl monitor targets to monitor the health status of NVDIMM and to notify critical status.

## Slide 31: Features of ndctl monitor (1/3)
SMART events come from NVDIMM can be monitored
SMART event | trigger | effect
spares-remaining | spare block value goes below the spare threshold limit | NVDIMM becomes broken; data will be lost; etc.
health-status | normal health status of NVDIMM changes | 
unclean-shutdown | last shutdown to be recorded at the next boot | saving data target failed on NVDIMM; etc.
media-temperature | temperature value of nvdimm goes above threshold limit | server is getting too hot; may need remediation; a specific fan fails; etc.,
controller-temperature | controller temperature value goes above threshold limit | 
Notes: Now let’s come to the features of Ndctl monitor. The first feature is that it supports multiple SMART health event. My original idea was only to monitor the SMART health event which was dimm spare remaining. However, after discussing with the maintainer Dan Williams for several times, we decided to make a platform that supports more SMART events. Currently these SMART events that come from NVDIMM can be monitored.

## Slide 32: Features of ndctl monitor (2/3)
Actions after monitoring
  Log the output notification
    Log destination
      syslog
      arbitrary file （set in the configuration file or set by command option）
    Output format
      JSON (can be analyzed by other log collectors, such as fluentd）
  Kick other application（to be implemented）
    When the monitor detects a SMART health event, the application will move the data in real time.
Notes: The second feature is that there are several actions after monitoring. One is to log the output notification. As to log destination, users can set it to syslog or an arbitrary file, which can be set in the configuration file or be set by command option. As to output format, it is based on JSON, which can be analyzed by other log collectors, such as fluentd. The other action is to kick applications. This is not finished. Via this action, when the monitor detects a SMART health event, the application will move the data in real time.

## Slide 33: Features of ndctl monitor (3/3)
Filter of ndctl monitor
  objects to monitor can be filtered
    all NVDIMMs are monitored by default
    objects can be filtered by namespace, region, bus, and dimm
      backup the data of applications which are running on a certain namespace ⇒ filter by namespace
      allowing to monitor for any media error on the bus ⇒ filter by bus
  SMART health events to monitor can be filtered
Notes: The third feature is the filter of ndctl monitor. Objects to monitor and SMART health events can be filtered. ALL NVDIMMs are monitored by default. Meanwhile objects to monitor can be filtered by namespace, region, bus, and dimm. For example, when users need to backup the data of applications that are running on a certain namespace，they can use filter by namespace.

## Slide 34: ACPI supports for NVDIMM
NVDIMM has SMART Health Info like SSD/HDD
  SMART Health Info can be retrieved via a _DSM method
  SMART Health Info includes spare block value and spare threshold limit
ACPI 6.1 adds “NFIT Health Event Notification”
  a notification will be sent when the spare block value goes below the spare threshold limit
  a poll(2) event will be triggered when the notification is received
NFIT Health Event Notification
triggers a poll(2) event on /nmemX/nfit/flags
spare block value below threshold
ACPI (Firmware)
NVDIMM (Hardware)
Kernel (OS)
Notes: Next, I would like to introduce what ACPI supports for monitoring the health status of NVDIMM.
First, as goto-san mentioned, NVDIMM has SMART data like SSD. The NVDIMM driver can use a _DSM method to retrieve current SAMART status of each NVDIMM. And, SMART Health information includes spare block value and spare threshold limit. Second, As ACPI 6.1 adds an “NFIT Health Event Notification” for NVDIMM Devices. If the current spare block value goes below the spare threshold limit, notification will be sent. A poll event on the nmem/flags sysfs attribute will be triggered when the notification is received.

## Slide 35: Architecture of ndctl monitor
triggers a poll(2) event on /nmemX/nfit/flags
output notification
filter health event(s) to monitor
retrieve NVDIMM SMART status
Kernel (OS)
ndctl monitor
standard output, syslog, /var/log/ndctl/monitor.log etc.
monitor poll(2) event(s) on /nmemX/nfit/flags
filter object(s) to monitor
retrieve NVDIMM SMART status
Notes: This figure shows the architecture of ndctl monitor. At first please look at the middle part in green, which shows the processing of monitor. When monitor starts up, it filters the NVDIMMs to monitor via reading configuration file. Then, it retrieves the current SMART status of each NVDIMM. If there is nothing wrong with the NVDIMMs, it starts to monitor poll events on /nmemX/nfit/flags. Now look at the red part in the bottom plz. When kernel triggers a poll event on /nmemX/nfit/flags, it will be monitored out.
Then the monitor will retrieve the current SMART status of NVDIMM which fired SMART health event. the health event can be distinguished by comparing SMART health status. Then, monitor will filter health event. If this event is what users want to monitor, it will output a notification.

## Slide 36: Sample of output notification
"timestamp":"1537323709.432459532",
"pid":28189,
"event":{ "dimm-spares-remaining":true },
"dimm":{
"dev":"nmem1", "health":{
"health_state":"non-critical",
"temperature_celsius":23,
"controller_temperature_celsius":25,
"spares_percentage":4,
"temperature_threshold":40,
"controller_temperature_threshold":30,
…
"spares_threshold":5,
"shutdown_state":"clean“
}
}
current spare block value
spare threshold limit
SMART Health event
Notes: Here is a sample of output notification. As I said, this notification obeys JSON format. We can acquire information about time, pid, health event, and current SMART status of NVDIMM from this notification. Please look at the red line, the current spare block value is 4 percent and the spares threshold limit is 5 percent. The spare block value is lower than threshold limit. So this dimm-spare-remaining notification could be sent.

## Slide 37: How to start ndctl monitor
Linux distribution support systemd
  Systemd service
  ⇒ systemctl start ndctl-monitor.service
Linux distribution does not support systemd
  ndctl monitor --daemon
Users could run monitor as a one shot command
  ndctl monitor
Notes: Now I would like to talk about how to start Ndctl monitor. When the linux distribution supports systemd, users can start monitor by this command.
When the linux does not support systemd, users can run ndctl monitor as a daemon by using --daemon option. For users who want to run monitor as a one shot command, they can run this ndctl monitor command.

## Slide 38: Demo
Notes: Here is a demo, which shows the way monitor works.

## Slide 39: Summary and Future work
Summary
  Basis of NVDIMM
  Replacement
    Replacement of NVDIMM is complex
    Adding some information in ndctl list for replacing NVDIMM
  Monitoring
    Monitoring SMART status of NVDIMM is important
    Ndctl monitor daemon
Future work
  Kicks other applications by daemon
  plural daemon execution via systemctl
Notes: Now I will give a brief summary of the speech.
At the first we introduced the basis of NVDIMM. Then we talked about two issues that we found and solved.
One is the replacement of NVDIMM. The other one is the monitor NVDIMM.
And, at the end, here are some plans about our future work.
Thank you for your time.

## Slide 41: Emulation of NVDIMM
You can try NVDIMM interface easily
  custom e820
    To try interface for filesystem or DAX
    it can used with kernel boot option (memmap=XXG!YYG)
      XX Gbyte RAM is used for NVDIMM interfaces
  nfit_test.ko
    Try to test management command (ndctl)
    It works instead of the firmware for NVDIMM

## Slide 42: Types of NVDIMM
JEDEC defines some types of DIMM module
NVDIMM-N
DIMM module includes DRAM and NVMEM
NVDIMM-F
Only NVMEM is used
access like storage
NVDIMM-P
DIMM module includes DRAM and NVMEM
Amount of RAM is less than NVMEM
Amount of RAM = Amount of NVMEM
The module includes battely
Backup to NVMEM at Power down
RAM is used as cache
Usually, RAM is used
DRAM
NVMEM
battery
DRAM
NVMEM
NVMEM